## Slide 1: MINI-WAY
Two-wheeled self-balancing robot

## Slide 2: Content
Introduction
1
Project Management
2
Requirement
3
Hardware Design
4
Algorithms & Implement
5
Testing & Results
6
Conclusion
7
MINI-WAY

## Slide 3: Content
Idea
Advantages
Existing products
Scope
Introduction

## Slide 4: Idea
Human’ balance
Balance
Fall
Balance a stick
Balance a stick
Segway automatic electric vehicle
Two-wheeled self-balancing robot
Introduction

## Slide 5: Advantages
Environment-friendly
  Narrow traffic
Easy to use
  Commodity transferring
Strange Style
Medium Price
Text
Introduction

## Slide 6: Advantages(cont.)
Platform for the develop humanoid robot
Complement movement technology solution
Introduction

## Slide 7: Existing products
Nicola’s robot
  CPU: Arduino diecimila
  Actuators: 2 * EMG30
  Sensors: IMU sensor
  Cost to build: $350
DIY Segway
  Controller: AtMega168
  Sensors :
    ADXRS614
    ADXL203
  Cost to build: ~$400
Introduction

## Slide 8: Scope
Create small scale model similar to Segway:
  High: 50cm
  Overall Footprint :15cm x 30cm
Budget: $150
Schedule: 4 months
MINI-WAY clay model
Introduction

## Slide 9: Content
Project Information
Project Team
Project Model
Plan
Risk
Communication
Project Management

## Slide 10: Project Information
Project Name: MINI-WAY
Project code: MINI-WAY
Production type: Two-wheeled self-balancing robot
Timeline: From December 2012 to April 2013
Project Management

## Slide 11: Project Team
HieuNN
PM/Dev
HungPD
Supervisor
TruongNM
Des/Dev
LamVV
Dev/Test
QuyTK
T&QA
Project Management

## Slide 12: Project Model
Iterative and Incremental Development
Project Management

## Slide 13: Plan
Project Management
Initiation & Planning
Execution
Technical Analysis
Monitoring & Closing
Monitoring
Project Introduce
SRS
Closing
Create Plan
Design
Implementation
Testing
Result
Deployment
16 days
14 days
83 days
Miniway_Project Plan

## Slide 14: Risk
Difficulty in:
  Design hardware
  Control time to purchase devices, printed circuit
  Implement theory
Project Management

## Slide 15: Communication
Work offline five days per week at lab room.
Other : Email, Phone, yahoo, Facebook
Project Management

## Slide 16: Content
Requirement
Function Requirement
Non-functional Requirement
Mechanical Design

## Slide 17: Function Requirement
Function name | Auto balancing
Description: | The robot maintains balance position by moving forward or backward.
Normal Course of Events: | Place the robot on a flat surface and hold it in balance position Switch power ON Let the robot move arround freely
Special Requirements: | The robot must not venture more than 70 centimeters from starting point. Vertical position must not exceed 30 degree
Requirement
Function name | Rebalance
Description: | The robot need to recover itself from external disturbance
Normal Course of Events: | The robot is powered on and maintaining balace position Use hand to alternate it anglular postion Let the robot rebalace
Special Requirements: | The robot must not regain balace postion while not moving more than 1.5 meter from starting point. In case of unable recovery, the robot should perform auto shutdown or temporary disable its electric motor

## Slide 18: Non-functional Requirement
Requirement
    Performance
Power-on setup time is less than two second.
Drift no more than 5 degrees from set-point while standing.
    Serviceability
All component could be disassemble and reassemble by hand tool, no special equipment required.
Accumulated operating time before major repair: 1 week.
    Reliability
Onboard firmware should be able to run at least 2 hours continuously without the need of manual or auto reset.
    Cost
Total build cost is less than 300$.
    Safety
Electronics and mechanical part is well secured.
All connector and electrical join is insulated.

## Slide 19: Mechanical Design
Requirement

## Slide 20: Mechanical Design(cont.)
Requirement

## Slide 21: Mechanical Design(cont.)
Requirement

## Slide 22: Mechanical Design(cont.)
Requirement

## Slide 23: Content
System Architecture
Block Diagram
Tools
Devices
Controller Broad Design
  Printed Circuit
  Final board
Hardware Design

## Slide 24: System Architecture
Hardware Design

## Slide 25: Block Diagram
Hardware Design

## Slide 26: Tools
Hardware Design

## Slide 27: Devices
Microcontroller
  Fast 16-bit microprocessor
  48 Kbytes on-chip Flash
  1 x I2C module
  2 x UART modules
  4 x PWM output
  Low power consumption
dsPIC30F4013 30I/P
Hardware Design

## Slide 28: Devices(cont.)
IMU Sensor
  Triple Axis Accelerometer
  Triple Axis Gyroscope
  IIC Communication
  Operate at 3.3/5v
  Easy to configure
GY-86 (MPU6050-HMC5883l-MS5611)
Hardware Design

## Slide 29: Devices(cont.)
Bluetooth module
  Long range, high sensitivity
  Bluetooth 2.0 compatible
  UART Interface
  Easy to configure with AT command
HC-06 Bluetooth module
Hardware Design

## Slide 30: Devices(cont.)
Motor controller
  Operating supply voltage of up to 46V
  Total DC current of up to 4A
  Accept standard TTL logic levels
  Over-temperature protection
L298N dual H-Bridge motor driver
Hardware Design

## Slide 31: Devices(cont.)
Motor
  Operate at 12 Volt
  Compact
  Built-in encoder
12 volt brushed DC motor with planetary gearbox
Hardware Design

## Slide 32: Devices(cont.)
Battery
  High capacity
  High discharge rate
  Small and light
Turnigy 2200mAh 3S 20C Lipo Pack
Hardware Design

## Slide 33: Controller Broad Design
Microcontroller and headers
Power supply
Dual motor driver
Hardware Design

## Slide 34: Controller Broad Design(cont.)
Hardware Design

## Slide 35: Controller Broad Design(cont.)
Hardware Design

## Slide 36: Controller Broad Design(cont.)
Hardware Design

## Slide 37: Controller Broad Design(cont.)
Hardware Design

## Slide 38: Printed Circuit
Hardware Design

## Slide 39: Final board
Hardware Design

## Slide 40: Content
Algorithms
Implement
Experiment
Algorithms & Implement

## Slide 41: PID Algorithm
PID – Proportional Integral Derivative
Equation:
Where
Algorithms
Symbol | Description
 | Set-point: the balance position of the robot
 | Process variable: the position of the robot
 | Output
 | Proportional term
 | Integral term
 | Derivative term
 | Error = SP - PV
 | Time
Symbol | Description
 | Set-point: the balance position of the robot
 | Process variable: the position of the robot
 | Output
 | Proportional term
 | Integral term
 | Derivative term
 | Error = SP - PV
 | Time

## Slide 42: PID Controller
PID controller for balancing robot:
Algorithms

## Slide 43: Tilt Angle Calculation
Algorithms
Angle: 𝜃 = (code: 𝜃 = 𝜃 + 𝜃 * Sample period)
𝜃 = (180/Pi) * Arctan[ Rx/SQRT(Ry2 + Rz2) ]

## Slide 44
Gyro Angle Drift
Algorithms

## Slide 45: Accelerometer Angle fluctuate
Algorithms

## Slide 46: Filter
Algorithms
Complementary Filter

## Slide 47: Complementary Filter
Algorithms

## Slide 48: Firmware
System Flowchart:
Implement

## Slide 49: Firmware
Initiate Process:
Implement

## Slide 50: Firmware
Balancing Process:
Implement

## Slide 51: Firmware
Complimentary Filter Process:
Implement

## Slide 52: Firmware
PID Calculator Process:
Implement

## Slide 53: Firmware
Motor Controller Process:
Implement

## Slide 54: PID Tuning
Step 1: Tuning only Proportional term (Ki = 0, Kd = 0).
Step 2: Using Ziegler-Nichols method equations:
Where
Step 3: Correction Kp, Ki, Kd.
Experiments
Symbol | Description
 | Ultimate gain of Kp
 | Oscillation period
Symbol | Description
 | Ultimate gain of Kp
 | Oscillation period

## Slide 55: PID tuning
Tuning with
Experiments

## Slide 56: PID tuning
Tuning with
Experiments

## Slide 57: PID Controller
With
Experiments

## Slide 58: PID Controller
With
Experiments

## Slide 59: PID Controller
With
Experiments

## Slide 60
Test Plan
Test Item Example
Test report
Test result
Content
Testing & Results

## Slide 61
Test Plan
Testing & Results
Device testing
Unit test
Function test
System test

## Slide 62
Test Item Example
Testing & Results

## Slide 63
Test Report
Testing & Results

## Slide 64
Test Result
Testing & Results
 | Device test | Unit test | Integration test | System test | Total
Pass | 18 | 21 | 20 | 8 | 100%
Fail | 0 | 0 | 0 | 0 | 0%
Untested | 0 | 0 | 0 | 0 | 0%
Total | 18 | 21 | 20 | 8 | 100%
Test result:
Bug result:
 | Device test | Unit test | Integration test | System test | Total
Fixed | 3 | 1 | 1 | 0 | 83.33%
Fail | 0 | 0 | 1 | 0 | 16.67%
Total | 3 | 1 | 2 | 0 | 100%

## Slide 65
Limitation
Perspective
Demo
Content
Conclusion

## Slide 66
Limitation
Conclusion
  For now, MINI-WAY robot can just auto balancing only on a flat surface.
  The robot is still a small model for two wheel balancing robot. The robot can just carry small thing that is not too heavy.

## Slide 67
Perspective
Conclusion

## Slide 68
Demo
Demo
Conclusion

## Slide 69
Thank You !