## Slide 1: Product Counting System on Conveyor Belt
Capstone Project – PCSCB Team

## Slide 2: Contents
Introduction
Requirements
Design
Identification
Test
Conclusion
Demo
Q&A

## Slide 3: 1. Introduction
Idea
Scope
Project Management Plan
Member’s role
Communication
Resource Needed

## Slide 4: 1.1 Idea
Low cost
Easy to use
Easy to deploy
High accuracy

## Slide 5
Camera + Barcode

## Slide 6
Ultrasonic sensor + Camera

## Slide 7: 1.2 Scope
Use ultrasonic sensor
Apply Neural Network (NN) as main approach

## Slide 8: 1.3 Project Management Plan
Iterative model

## Slide 9: 1.3 Project Management Plan

## Slide 10: 1.4 Member’s role
Supervisor
PM/Dev
Tech Lead
Test/
Design
Dev/
Test
Dev/
Test

## Slide 11: 1.5 Communication
Work offline five days per week at lab room.
Others: Email, Phone, Skype.

## Slide 12: 1.6 Resource needed

## Slide 13: 2. REQUIREMENTS
Functional requirements
Non-functional requirements

## Slide 14: 2.1 Functional requirements
3 functions: Collecting data sample, Training, Counting
6 Cases:

## Slide 15: 2.2 Non-functional requirements
System response: < 0.5 s
High accuracy: 100% with constraints of project
Easy to deploy
Easy to use
Low cost, easy to maintain

## Slide 16: 3. design
Proposed system architecture
Mechanic design
Circuit design

## Slide 17: 3.1 Propose system architecture
Physical architecture

## Slide 18: 3.1 Propose system architecture
PC application & relation

## Slide 19: GUI Design

## Slide 20: 3.2 Mechanic Design
  Software Designer

## Slide 21: 3.2 Mechanic Design
    Conveyor Belt Prototype Design

## Slide 22: 3.2 Mechanic Design
  Real

## Slide 23: 3.2 Mechanic Design
Finally

## Slide 24: 3.3 Circuit Design
Components
HC-SR04 ultrasonic sensor
Omron E4PA-LS600-M1-N
SRF05 ultrasonic sensor

## Slide 25: 3.3 Circuit Design
PIC-18F4620
LM1117MP
PL2303HX

## Slide 26: 3.3 Circuit Design
Designer Software

## Slide 27: 3.3 Circuit Design
Schematic

## Slide 28: 3.3 Circuit Design
PCB (Printed Circuit Board)

## Slide 29: 4. Identification
Pre-processing of signal
Introduction to NN
Features
Training the NN
Versions of training data

## Slide 30: 4.1 Pre-processing of signal
Raw data

## Slide 31: 4.1 pre-processing of signal
Median filter

## Slide 32: 4.1 Pre-processing of signal
Double exponential smoothing
  Ft = a* At-1 + (1- a) * (Ft-1 + Tt-1)
  Tt = b* (At-1-Ft-1) + (1- b) * Tt-1
  AFt = Ft + Tt
  With Ft: Unadjusted forecast (before trend)
  Tt: Estimated trend
  AFt: Trend-adjusted forecast
  a, b: weight between 0 and 1

## Slide 33: 4.1 Pre-Processing of signal
Final results

## Slide 34: 4.2 Introduction to NN
What is Neural Network
How to train neural network

## Slide 35: 4.2.1 What is Neural Network
A layered network consists of nodes or neurons with training weights.

## Slide 36: 4.2.2 How to train NN
Flash Demo
http://inquiry.ucsd.edu/flash/simpleNNBP.html

## Slide 37: 4.3 Features
Core Pattern
Histogram
Measurements

## Slide 38: 4.3.1 Core Pattern
The “valley” between two consecutive products is the decisive pattern in recognition process

## Slide 39: 4.3.2 Histogram

## Slide 40: 4.3.3 Measurements

## Slide 41: 4.4 Training the Neural Network
Training Cases
Analyze and Construct Training Data

## Slide 42: 4.4.1 Training Cases
One product
Two products

## Slide 43: 4.4.2 Analyze and Construct Training Data
Raw data graph
Chart: Raw data
Cut into smaller windows

## Slide 44: 4.4.2 Analyze and Construct Training Data
Chart: 
View of a single window
Get measurements
Chart: 

## Slide 45: 4.4.2 Analyze and Construct Training Data
Extracted histograms from windows
Chart: Distances
| 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
Distance | 5 | 1 | 6 | 7 | 6 | 5 | 66 | 34
Get histograms

## Slide 46: 4.4.2 Analyze and Construct Training Data
Raw data in the representation of histograms
Chart: 
Pattern revealed!

## Slide 47: 4.5 Versions of Training Data
Version 1: Only Histograms
Version 2: High Resolution Histograms
Version 3: Trimmed Histogram with Measurements

## Slide 48: 4.5.1 Version 1: Only Histograms
The training inputs only consist of a histogram with size of 130 and 8 fields.
Pick 3 histograms that represent the graph of a product at it left most, middle and right most position.
The purpose is to test the ability to recognize between whether the conveyor belt has product or not.

## Slide 49: 4.5.1 Version 1: Only Histograms
43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | Class
0 | 0 | 0 | 0 | 0 | 0 | 75 | 55 | 0
0 | 0 | 0 | 0 | 0 | 0 | 77 | 53 | 0
0 | 0 | 0 | 0 | 0 | 0 | 76 | 54 | 0
0 | 0 | 0 | 0 | 0 | 0 | 80 | 50 | 0
0 | 0 | 0 | 0 | 0 | 0 | 79 | 51 | 0
43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | Class
4 | 3 | 8 | 12 | 5 | 3 | 76 | 19 | 1
4 | 3 | 8 | 12 | 5 | 3 | 68 | 27 | 1
4 | 3 | 8 | 12 | 5 | 3 | 71 | 24 | 1
7 | 18 | 7 | 5 | 4 | 4 | 85 | 0 | 1
7 | 18 | 7 | 5 | 4 | 4 | 65 | 20 | 1
Chart: Middle
Chart: Right most
Chart: Left most

## Slide 50: 4.5.1 Version 1: Only Histograms
How to visualize Neural Network outputs

## Slide 51: 4.5.1 Version 1: Only Histograms
Statistic training results:
  Training samples: 90
  Classification accuracy: 1
  Error rate: 0
Real data test:
  Only 2 cases of none product was detected
  No distinct recognition at all!!!

## Slide 52: 4.5.2 Version 2: High Resolution Histograms
Increase the resolution of histogram to 0.5 cm.
Pick a set of histograms which shifts from left most to right most position
Increase the number of recognition class to three (one, two or none product)

## Slide 53: 4.5.2 Version 2: High Resolution Histograms
43 | 43.5 | 44 | 44.5 | 45 | 45.5 | 46 | 46.5 | 47 | 47.5 | 48 | 48.5 | 49 | 49.5 | 50 | One | Two | None
0 | 0 | 4 | 5 | 3 | 1 | 1 | 2 | 1 | 2 | 1 | 1 | 0 | 1 | 68 | 0 | 0 | 1
0 | 0 | 0 | 6 | 2 | 6 | 1 | 0 | 1 | 1 | 1 | 2 | 2 | 5 | 63 | 0 | 0 | 1
0 | 0 | 1 | 6 | 6 | 1 | 1 | 0 | 1 | 1 | 1 | 2 | 2 | 5 | 63 | 0 | 0 | 1
0 | 0 | 0 | 6 | 4 | 5 | 3 | 2 | 1 | 1 | 1 | 2 | 2 | 5 | 58 | 1 | 0 | 0
0 | 0 | 0 | 0 | 5 | 10 | 3 | 2 | 1 | 1 | 0 | 1 | 1 | 1 | 65 | 1 | 0 | 0
0 | 0 | 0 | 0 | 5 | 10 | 3 | 2 | 0 | 1 | 2 | 1 | 2 | 5 | 59 | 1 | 0 | 0
9 | 7 | 7 | 10 | 15 | 13 | 5 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 16 | 0 | 1 | 0
9 | 7 | 7 | 10 | 15 | 13 | 5 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 15 | 0 | 1 | 0
9 | 7 | 7 | 10 | 15 | 13 | 5 | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 14 | 0 | 1 | 0

## Slide 54: 4.5.2 Version 2: High Resolution Histograms
WRONG!
One
Two
One
Two
One
Two
One
Two
One
Two
One
Two
One

## Slide 55: 4.5.2 Version 2: High Resolution Histograms
Statistic training results:
  Training samples: 1892
  Classification accuracy: 0.979592
  Error rate: 0.0204082
Real data test:
  Only 2 / 13 cases are wrong
  84% accuracy on real data test

## Slide 56: 4.5.3 Version 3: Trimmed Histogram with Measurements
Do a little statistic analysis on the training data
Statistics | 43 | 43.5 | 44 | 44.5 | 45 | 45.5 | 46 | 46.5 | 47 | 47.5 | 48 | 48.5 | 49 | 49.5 | 50
Standard Deviation | 1.560886 | 3.303085 | 4.744917 | 4.317798 | 2.61962 | 1.561252 | 1.326804 | 1.09453 | 2.114539 | 0.99212 | 0.783453 | 1.045937 | 1.416573 | 2.436769 | 21.10286
Average | 0.348741 | 1.594243 | 2.715195 | 2.341544 | 1.569333 | 1.071132 | 0.846942 | 0.846942 | 1.071132 | 0.747301 | 0.672571 | 0.822032 | 1.145862 | 2.042624 | 72.16441
Min | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10
Max | 10 | 16 | 17 | 21 | 11 | 5 | 6 | 4 | 11 | 4 | 2 | 4 | 5 | 7 | 90

## Slide 57: 4.5.3 Version 3: Trimmed Histogram with Measurements
Reduce the distance between the sensor and the conveyor belt surface(from 50cm to 30cm)
Increase histograms resolution back to 1cm
Choose 4 the most noticeable distances
Sum the two top distances in the chosen four.
Combine with measurements

## Slide 58: 4.5.3 Version 3: Trimmed Histogram with Measurements
22 | 23 | 24 | 29 | 22 + 23 | Product length | Slopes length | Area
0 | 0 | 0 | 80 | 0 | 0 | 2.44E-12 | 7.05E-12
0 | 0 | 0 | 80 | 0 | 0 | 1.49E-12 | 4.61E-12
0 | 0 | 0 | 80 | 0 | 0 | 0.39 | 0.39
0 | 0 | 0 | 79 | 0 | 1 | 0.6279 | 1.0179
0 | 5 | 2 | 60 | 5 | 20 | 12.4813 | 77.8831
1 | 5 | 2 | 59 | 6 | 21 | 12.6887 | 84.5587
2 | 5 | 2 | 58 | 7 | 22 | 12.8153 | 91.3608

## Slide 59: 4.5.3 Version 3: Trimmed Histogram with Measurements
Statistic training results:
  Training samples: 2097
  Classification accuracy: 0.986667
  Error rate: 0.0133333
Real data test cases:
  V for 1 vertical product, H for 1 horizontal product
  5xV, 5xH, 5xVV, 5xHH, 5xVH, 5xHV

## Slide 60: 4.5.3 Version 3: Trimmed Histogram with Measurements
5 cases of
one vertical product are all recognized correctly!

## Slide 61: 4.5.3 Version 3: Trimmed Histogram with Measurements
5 cases of
one horizontal product are all recognized correctly!

## Slide 62: 4.5.3 Version 3: Trimmed Histogram with Measurements
5 cases of
two vertical product
are all recognized correctly!

## Slide 63: 4.5.3 Version 3: Trimmed Histogram with Measurements
5 cases of
two horizontal product
are all recognized correctly!

## Slide 64: 4.5.3 Version 3: Trimmed Histogram with Measurements
5 cases of
one vertical and one horizontal products
are all recognized correctly.
But there is one anomaly!

## Slide 65: 4.5.3 Version 3: Trimmed Histogram with Measurements
5 cases of
one horizontal and one vertical products
are all recognized correctly!

## Slide 66: 4.5.3 Version 3: Trimmed Histogram with Measurements
Real data test result:
99% accuracy

## Slide 67: 5. Test
Test strategy
Testing results

## Slide 68: 5.1 Test Strategy

## Slide 69: 5.2 Testing Result

## Slide 70: 5.2 Testing Result

## Slide 71: 6. Conclusion
Difficulties, Limitation, Strategy & Solution
Perspective
Lesson Learnt

## Slide 72
Difficulties
Lack of knowledge.
Differences between theory and reality.
Member’s skill are not the same so assigning works for each one.
Mechanic.
Limitation
Non-Technical problem
Technical problem
PCSCB limitations
Strategies and Solution
Solution for different conveyor belt’s speed problem.
Solution for poor sensor’s performance.

## Slide 73: 6.2 Perspective

## Slide 74: 6.3 Lesson Learnt
Learn how to approach the new technology
Learn how to make team working effect and improve communication skills.

## Slide 75: 7. DEMO

## Slide 76: 8. Q&A

## Slide 77: Thanks for listening